## Slide 1: 22th dec wednesday
Task:
A)
  2 leds and 2 push buttons are used as digital inputs and outputs.
  Initially both LEDs are off.
  After button 1 is pressed 4 times, blue LED will toggle after 200ms.
  After button 2 is pressed 6 times, red LED will toggle after 800ms.
  This procedure goes indefinitely.
  Switch bouncing should be avoided.
B)
  Repeat part (A), using 2 push butons as interrupt inputs.
Hint: For both tasks (A and B), you can begin with 1 led and 1 pb, then…

## Slide 2: 23th dec thursday
Task:
A)
  2 leds and 2 push buttons are used as digital inputs and outputs.
  Initially both LEDs are off.
  After button 1 is pressed 4 times (no time limit for pressing), blue LED will toggle.
  After button 2 is pressed 6 times (no time limit for pressing), red LED will toggle.
  This procedure goes indefinitely.
  Switch bouncing should be avoided.
B)
  Use a single push button as interrupt input, with two LED outputs. 4 and 6 presses within a definite time interval toggles LED1 and LED2 respectively.

## Slide 3: 29th dec wdsday
Task:
A)
  2 leds and 2 push buttons are used as digital inputs and outputs.
  Initially both LEDs are off.
  After button 1 is pressed 4 times (no time limit for pressing), blue LED will turn on and after pressed 4 times it will turn off.
  After button 2 is pressed 5 times (no time limit for pressing), red LED will turn on and after pressed 5 times it will turn off.
  This procedure goes indefinitely and switch bouncing should be avoided.
B)
  Use a single push button as an interrupt input, and two LEDs as outputs.
  Initially both LEDs are on.
  Count button press in a definite time interval (e.g. 1s).
  If count is 3, LED1 turns off for 300ms.
  If count is 5, LED2 turns off for 500ms.

## Slide 4: 30th dec thursday
Task:
A)
  2 leds and 2 push buttons are used as digital inputs and outputs.
  Initially both LEDs are off.
  After button 1 is pressed 4 times (no time limit for pressing), blue LED will turn on and after pressed twice it will turn off.
  After button 2 is pressed 5 times (no time limit for pressing), red LED will turn on and after pressed thrice it will turn off.
  This procedure goes indefinitely and switch bouncing should be avoided.
B)
  Use a single push button as an interrupt input, and two LEDs as outputs.
  Initially both LEDs are on.
  Count button press in a definite time interval (e.g. 1s).
  If count is 3, LED1 blinks 2 times.
  If count is 5, LED2 blinks 4 times.